## Slide 1: The LocoDrone
Providing an affordable platform for aspiring drone pilots to develop the necessary skills required for more advanced drones

## Slide 2: Concept
Custom transmitter and telemetry board capable of integrating with wide array of cheap drones already on the market
Customizable real-time control interface (ex. Joysticks, Accelerometer, etc.)
Programmable flight routines and sensor feedback via integration with the LocoRobo Academy
Closed-loop autopilot algorithm executed locally on transmitter
    Receive flight data from telemetry board
    Process Data
    Send high level control commands (Yaw, Throttle, Roll, Pitch) to drone

## Slide 3
Real-time control
Computer Control
Drone
Telemetry Board
Transmitter
Sensor Data
Telemetry Data
High-Level
Flight Commands
(Yaw, Throttle, Roll, Pitch)
Telemetry Data
Input
Joysticks, Accelerometer, Trims
Flight Modes, Keyboard Control,
Trims, Telemetry Visualization,
Programmable Flight Routines
Closed-Loop
Autopilot

## Slide 4: Drone
Utilize cheap toy drones with limited functionality
LocoRobo transmitter and telemetry board integration
Wireless RF link to transmitter
Programmable flight routines
Closed-loop autopilot

## Slide 5: Real-Time Control
Customizable user interface (Joysticks, Accelerometer, Etc.)
Low-latency Radio Control System
Multiple flight modes
  Head-free (absolute orientation)
  Altitude Hold
  Heading Hold
  Collision Avoidance
Basic Autopilot Routines (position hold, collision avoidance, Etc.)

## Slide 6: Telemetry Board
Custom sensor board to be mounted on drone
Real-time telemetry data feedback, for both processing and visualization
Wireless RF link to transmitter
Sensors:
  Accelerometer (Attitude)
  Gyroscope (Stability)
  Barometer (Altitude)
  Magnetometer (Compass)
  Infrared (Proximity)
  Ultrasonic (Proximity)

## Slide 7: Transmitter
Integrated and customizable real-time control user interface (Joysticks, Accelerometer, Etc.)
Dual RF Link
  Transmit flight commands to drone
  Receive flight data from telemetry board
Execute autopilot commands and telemetry data processing on transmitter hardware (instead of on the drone)
Can function as stand alone hardware (real-time control and autopilot only)

## Slide 8: Computer Control
Complete integration with the LocoRobo Academy
  Keyboard control and trimming
  Setting adjustment
  Programmable flight routines
  Telemetry data visualization
  Transmitter hardware lessons & tutorials
Programmable flight routines (Blocks, Python, MATLAB, Etc.)
Setting adjustment (Autopilot PID, Initial Setup, Etc.)
Telemetry data visualization (Graphs, Virtual Reality, Etc.)
Telemetry data processing (Custom Flight Modes, Etc.)
Closed-loop autopilot algorithms